CHECK LIST FOR REVIEW OF SURVEY PLATS

FOR COMPLIANCE WITH

MISSOURI STANDARDS FOR PROPERTY BOUNDARY SURVEYS

NAME OF SURVEYOR:  ________________________    DATE OF SURVEY:  _________

REVIEWED BY: _____________________________    	DATE: _________

DESCRIPTION OF SURVEY:  __________________________________________________

______________________________________________________________________________

______________________________________________________________________________

GENERAL LAND SURVEY REQUIREMENTS

ALL SURVEY PLATS SHALL SHOW THE FOLLOWING	YES	 NO	NA

1)	Name of person or entity for whom the survey was made 	____	____	____

2)	Date of the survey	____	____	____

- Lettering 0.08" or larger in height	____	____	____

# Direction of all lines surveyed with directional reference	____	____	____

- North arrow, written scale and graphic scale on each sheet	____	____	____

containing graphics

6)	Horizontal (ground) distances of all lines surveyed	____	____	____

in feet or meters

7)	All curved lines defined with minimum of two (2) elements	____	____	____

Additional directional component for non-tangential curves

8)	Definition of elevation datum	____	____	____

9)	Location and elevation of bench mark used	____	____	____

10)	Distance and area dimensions representative of actual precision	____	____	____

YES	 NO	NA

11)	Show or reference source of boundary description	____	____	____

12	Show property description of parcel created	____	____	____

13)	Subdivision plats identify all lots for sale by numbers	____	____	____

14)   Sufficient data to locate the property (distance and direction)           ____   ____    ____

within the USPLSS, or within record subdivision

15)	All controlling corners found and exterior corners found or set	____	____	____

identified on plat

16)  Any material variation between measured and record dimensions     ____    ____	   ____

and or between measured and lines of possession

17)	Reference source document(s) for pertinent data obtained in	____	____	____

records research

18)	Accuracy from type of property being surveyed	____	____	____

19)	Plat shall identify title documents for adjoiners as they appear	____	____	____

of record

20)	Statement that survey is in compliance with Missouri	____	____	____

Standards for Property Boundary Surveys

TITLE BLOCK CHECKLIST – 20 CSR 2030 – 2.050

The title block must, at a minimum, contain the following information

21) The name of the licensee either as a sole proprietor, partnership,

corporation, limited liability company, or other appropriate entity	____	____	____

22) The licensee’s address and phone number	____	____	____

23) Name or identification of project	____	____	____

24) Address/location of project (city/county and state)	____	____	____

25) Date prepared	____	____	____

26) Space for the licensee’s signature, date and seal	____	____	____

27) The printed name, discipline, and license number of the

person sealing the document	____	____	____

YES	 NO	NA

28) The printed name, discipline, and certificate of authority,                    ____	____	____

number of the corporation as defined in Section 327.011, RSMo.

WHEN THE MISSOURI COORDINATE SYSTEM 1983 IS USED

29)	Name of first or second order control station used	____	____	____

30)	Coordinates of control station (in meters) 	____	____	____

31)	Adjustment date and or epoch date 	____	____	____

32)  Brief statement of method used to obtain position	____	____	____

33)	Grid factor used 	____	____	____

ADDITIONAL REQUIREMENTS FOR SUBDIVISION SURVEYS

The recorded plat shall show

34)	Semi-permanent monuments at all exterior corners	____	____	____

35)	Two permanent monuments for every four acres developed	____	____	____

36)	Semi-permanent monuments at all lot corners.  All monuments	____	____	____

shall be set within twelve (12) months from date recorded.

REQUIREMENTS FOR CONDOMINIUM SURVEYS

37)	Name of condo		____	____	____

38)	Survey or general schematic map of entire condo	____	____	____

39)	Location and dimension of property not being developed,	____	____	____

and location and dimensions of all existing improvements

40)	Legal description of property being developed	____	____	____

41)	Extent of any encroachments	____	____	____

42)	Location of all easements	____	____	____

YES	 NO	NA

43)	Unless shown on plans, the following:

a)   Location and dimension of vertical unit boundaries	____	____	____

b)   Location and dimension of horizontal unit boundaries	____	____	____

c)   Unit identifying number	____	____	____

44)	Location and dimension of limited common elements	____	____	____

45)	Statement that plat contains information required	____	____	____

by Section 448.2-109

LOCATION OF IMPROVEMENTS - (WHEN REQUESTED)

46)	Permanent structures located by:

a)   Minimum of three dimensions	____	____	____

b)   Dimensions parallel or perpendicular to straight lines	____	____	____

c)   Dimensions radial to curved lines	____	____	____

LOCATION OF EASEMENTS - (WHEN REQUESTED) 	____	____	____

47)	Easements shown on subdivision plat	____	____	____

48)	Easements shown on other recorded documents and	____	____	____

provided to Surveyor by Client

GLO CORNER PRESERVATION AND REQUIRED FILING OF

CORNER FORMS

49)	Permanent monuments at GLO corners	____	____	____

50)	The following GLO corners were restored or reestablished	____	____	____

and registered with MDA / Land Survey Program

Township, Range, Corner Index Number

___________________________________________________	____	____	____

________________________________________________________	____	____	____

________________________________________________________	____	____	____

________________________________________________________	____	____	____

________________________________________________________	____	____	____